## Slide 1: Overview of NETCONF protocol
Notes: 2011-10-19
1

## Slide 2: Contents
Background to Netconf
Overview of Netconf
Netconf Standards
Data Classification and Data Stores
Notifications
COM / SGSN-MME support for Netconf
Further Information

## Slide 3
Background to Netconf
Overview of Netconf
Netconf Standards
Data Classification and Data Stores
Notifications
COM / SGSN-MME support for Netconf
Further Information

## Slide 4: Why Netconf? 1(2)
The first version of SNMP, SMI and MIB were released in 1988 as short term (draft) solutions for network management in the internet domain
It was anticipated that the long term solution would be CMOT (CMIP over TCP/IP) in order to converge with TMN standards
TMN + CMIP were regarded as technically superior to SNMP, but
  CMIP was complex, expensive to implement and resource hungry
  SNMP was simple to understand and easy to implement
Thus SNMP was widely accepted / implemented + formally approved as standards, while CMOT failed.

## Slide 5: Why Netconf? 2(2)
But … SNMP regarded as insecure and thus easy to hack
  It became widely used for for monitoring of alarms (based on notifications) and performance data (based on reading data)
  But limited use for configuration management
    Leading to a proliferation of proprietary CLI’s for CM
Following an IAB workshop in 2002, where several operators complained that IETF was not meeting their needs for CM, work was initiated which led to the Netconf standard

## Slide 6
Background to Netconf
Overview of Netconf
Netconf Standards
Data Classification and Data Stores
Notifications
COM / SGSN-MME support for Netconf
Further Information

## Slide 7: Overview of Netconf
Netconf protocol stack has 4 logical layers
Secure transport – not strictly part of Netconf but Netconf puts requirements on the transport layer, e.g. SSH or TLS
Messages – remote procedure calls (<rpc>, <rpc-reply>)
Operations – Netconf operations to read data (<get> or <get-config>, write data (<edit-config>), notifications etc.
Content – not strictly part of Netconf, e.g. ECIM or YANG models
Secure Transport
Messages
Operations
Content
Stack model
SSH
<rpc>
<get>
data
Stack example
All Netconf messages are complete XML documents
Standard encoding is UTF-8
  OSS-RC supports US-ASCII only
  ENM will support UTF-8

## Slide 8: Transport Layer
Any transport protocol which supports the Netconf requirements may be used.
  The requirements include that it should be connection oriented, secure, support long-lived sessions …
RFCs exist for Netconf over SSH, TLS, BEEP + SOAP
  BEEP + SOAP RFCs are now at historic status due to lack of interest
COM supports SSH transport from the beginning
COM 3.1 introduced support for TLS transport
  Current practice is that SSH is used by core nodes whereas TLS is used by radio nodes (Pico RBS + DUS Gen 2)
OSS-RC does not support changing of transport from SSH to TLS for a given node at runtime (requested by Pico RBS)
  Major impact on OSS, major reconfiguration of node, no business case
  ENM should consider supporting this (now also wanted by G2)

## Slide 9: Messages Layer - Capabilities
The level of Netconf support by a client or server is indicated by means of capabilities.
When a Netconf session is established the client and server “advertise” their capabilities in <hello> messages
Only capabilities, + capability versions, supported by both client and server may be used during the session
<hello xmlns=” urn:ietf:params:xml:ns:NETCONF:base:1.0”> <capabilities> <capability>urn:ietf:params:NETCONF:capability:base:1.0</capability> <capability>urn:ietf:params:NETCONF:capability:writable-running:1.0</capability> <capability>http://mycompany.com/mydevice/my-capability/2.5</capability> </capabilities> <session-id>387</session-id> </hello>

## Slide 10: Messages Layer - RPCs
NETCONF RPC communication consists of a sequence of <rpc> and <rpc-reply> elements encoded in XML.
  The client sends a request by means of an <rpc> element.
  The server responds with an <rpc-reply> element indicating success or failure.
The <rpc> element must include a “message-id” attribute.
  A string which contains an integer value.
  Incremented each time a new <rpc> element is sent by the client.
  Returned unaltered in the <rpc-reply> element
  Purpose is to link the reply with the associated <rpc> request
An <rpc-reply> may include an <ok>, <rpc-error> or <data> response

## Slide 11: Operations Layer
These are the typical operations that a management system wants to perform to read data <get> or <get-config>, write data <edit-config>, subscribe to notifications <create-subscription> etc.
A device indicates its level of Netconf support by means of capabilities
  Base capability is the minimum level of support for Netconf!!
    COM + SGSN-MME do not fully support the base capability.
  Optional capabilities are defined in the IETF standards
  Additional proprietary capabilities may be defined
A capability may introduce
  Additional operations and behaviour, updates to base operations
  Additional notifications
  Additional configuration data stores …

## Slide 12: Messages + Operations example
<rpc message-id=”567” xmlns=” urn:ietf:params:xml:ns:NETCONF:base:1.0”> <get-config> <source> <running/> </source> </get-config> </rpc> <rpc-reply message-id=”567” xmlns=” urn:ietf:params:xml:ns:NETCONF:base:1.0”> <data> … </data> </rpc-reply>
- The <rpc> requests the retrieval of data from the Netconf agent (server)
- The <rpc-reply> includes the requested data

## Slide 13: Data Layer
This is transparent to the Netconf protocol
YANG has been specified by IETF as a means to define data models to be exchanged over Netconf
YIN is the equivalent XML representation of a YANG module
A number Yang data modules have been defined by IETF and more are in the pipeline
From Ericsson perspective the data layer is an XML representation of ECIM models (based on the ECIM metamodel)
  ECIM metamodel is equivalent to Yang
  Mp.dtd is equivalent to YIN

## Slide 14
Background to Netconf
Overview of Netconf
Netconf Standards
Data Classification and Data Stores
Notifications
COM / SGSN-MME support for Netconf
Further Information

## Slide 15: Netconf + Yang Standards
Secure Transport
Messages
Operations
Content
Netconf
RFC 4741/6241
Netconf over SSH
RFC 4742/6242
Netconf over TLS
RFC 5539
Event Notifications
RFC 5277
Partial Lock
RFC 5717
With Defaults
RFC 6243
Yang
RFC 6020
Base Notifications
RFC 6470
Yang Data Types
RFC 6021
Access Control
RFC 6536
Netconf Monitoring
RFC 6022
SMIv2 to Yang
RFC 6643
Yang to DSDL
RFC 6110

## Slide 16
Background to Netconf
Overview of Netconf
Netconf Standards
Data Classification and Data Stores
Notifications
COM / SGSN-MME support for Netconf
Further Information

## Slide 17: Configuration vs state data
Configuration data is data which a NETCONF manager can write to a device in order to configure its behaviour.
State data is data produced by the device which a NETCONF manager may only read to evaluate how the device is performing.
  This may include status information, which indicates the current state of the device, and statistical information, which gives an indication of the device’s performance over time.
COM perspective (see COM Netconf IWD for full definition)
  RW data is configuration data
  RO data is state data
  OSS-RC always uses <get> operation and not <get-config>

## Slide 18: Configuration Data Stores
A configuration datastore is the complete set of data used to change a node from its initial state to a desired state.
The default datastore is running – the active configuration
The optional candidate datastore is like a planned area on the node
  Data is edited in the candidate datastore and then committed to the running datastore
  The optional validate capability allows the candidate to be validated
  The optional confirmed-commited capability allows a 2-phase commit of the candidate configuration to the running configuration
The optional start-up datastore is a specific configuration for initial start-up or restart of the node
  The running configuration must be copied to the startup datastore to make it persistent

## Slide 19: Writable-Running / persistent (Pico RBS + “CBA” nodes - WCG, DSC …)
OSS
running
NM/NMA
Planned
area
Valid
area
<edit-config>
data changes are persistent
Node

## Slide 20: Writable-Running / non-persistent (EPG, SSR)
OSS
running
NM/NMA
Planned
area
Valid
area
<edit-config>
data changes are not persistent
startup
Effectively there is a separate
startup configuration on the
node, but not accessible via
Netconf (only via CLI)
Node
A BNET PEST study on support
for the startup capability is up
for review at O&M Forum and
IAC in the next few weeks
2. <copy-config>
data changes are persistent

## Slide 21: Candidate / non-persistent (SGSN-MME)
OSS
running
NM/NMA
Planned
area
Valid
area
startup
Effectively there is a separate
startup configuration on the
node, but not accessible via
Netconf (only via CLI)
candidate
1. <edit-config>
2. <validate>
3. <commit>
data changes are not persistent
Node
A BNET PEST study on support for the startup
capability is up for review at O&M Forum and
IAC in the next few weeks.
SGSN-MME may support startup in 15B
4. <copy-config>
data changes are persistent

## Slide 22
Background to Netconf
Overview of Netconf
Netconf Standards
Data Classification and Data Stores
Notifications
COM / SGSN-MME support for Netconf
Further Information

## Slide 23: Why are notifications needed?
OSS-RC / ENM maintains a copy of the node data to enable its use cases, provide efficient responses to user requests etc.
When OSS first connects to a node it reads all the supported node data with a Netconf <get> operation
In order to keep the OSS copy of the data up to date (in sync with the node) the node is required to send Netconf notifications when any node data of interest is updated.
OSS-RC / ENM
node
node
node
<get>
<get>
<get>
<notification>
<notification>

## Slide 24: What kind of notifications?
Managed Object Created
  When an MO is created, and n attributes are set as part of the MO creation, the node shall send a single<objectCreated> notification which includes the name and value of each attribute which was set.
  This applies to attributes modelled as restricted or notifiable
  An attribute shall be included in the notification regardless of whether the attribute is assigned a value or set to its default value.
Managed Object Deleted
  When an MO is deleted the node shall send a single <objectDeleted> notification which includes the key (MO-id) attribute name and value.
  No other attributes shall be included in the notification.

## Slide 25: What kind of notifications?
AVC (Attribute Value Changed)
  When an MO is modified, and n attribute values are changed as part of the MO modification, the node shall send a single <AVC> notification which includes the name and value of each attribute whose value has changed.
  This applies to all attributes which are modelled as notifiable.
  An attribute shall be included in the notification if the attribute is assigned a new value, reset to its default value or unset.

## Slide 26: Standard Netconf Notification Behaviour - RFC5277
The Netconf Manager opens a session towards a Netconf agent
  Netconf manager and agent exchange capabilities via <hello> messages
  Support for notifications is indicated via the “notification” capability
A notification event subscription is requested using a <create-subscription> operation. Parameters include:
  <stream> : which streams of events is of interest
  <filter> : which subset of events is of interest
  <startTime> : used if replay of past notifications is required
  <stopTime> : used if subscription has a known end time, for example only replay of past notifications is required
    This is generally not of interest to OSS as it typically wants a replay + any future notifications

## Slide 27: Standard Netconf Notification Behaviour - RFC5277
The NETCONF session stays open for the lifetime of the subscription
  This is potentially months or years
  If the session is closed for any reason the subscription is deleted
RFC 5277 also defines an interleave capability whereby notifications and operations may be “interleaved” on the same Netconf session
  Not supported by COM or SGSN-MME
  Not wanted by OSS

## Slide 28: Streams
An event stream is “a set of event notifications matching some forwarding criteria”
Streams are predefined on a device
  Default stream is “NETCONF”
  This is the only stream supported by COM + SGSN-MME
Streams may be discovered using a <get> operation with filter. For each stream the response indicates:
  Name
  Description
  Replay Support (true or false)
  Replay log creation time (oldest available notification), if replay is supported.

## Slide 29: Supported notifications
Standard (RFC5277 notification capability)
  <replayComplete> : replay of older notifications is completed
  <notificationComplete> : requested stopTime has been reached
Proprietary
  COM notification capability (also supported by SGSN-MME)
    <replayTimeUnsupported> : requested startTime is earlier than oldest notification in replay buffer
      replay will proceed with oldest available notification
    <CMSychronizationRecommended> : due to restart of ME or notification buffer overflow
    <objectCreated> , <objectDeleted> , <AVC> : CM change notifications
  SGSN-MME heartbeat capability
    <heartbeat> : indicates that notification subscription is still active

## Slide 30: Netconf Notifications – Support in COM
Supported since COM 2.2 (sort of)
  Netconf + CLI requests intercepted by COM + notifications sent
    Changes made via other NBIs, or by the ME itself not notified
  COM 3.1 introduced an SPI for middlewares to report notifications
    Supported by pRBS 13B (O13B)
    Support by G2 / TCU 14B (O14B.1)
    Supported by COM-SA 3.2 + CMW 3.2 (O14A)
      But notification support in “CBA based nodes” like DSC, WCG etc. is not complete / trustworthy until 15A
        Audit of notification support in CBA planned for week 24
Supported in SGSN-MME since 14A

## Slide 31
Background to Netconf
Overview of Netconf
Netconf Standards
Data Classification and Data Stores
Notifications
COM / SGSN-MME support for Netconf
Further Information

## Slide 32: Netconf protocol standards
RFC Standard | EAG | COM | SGSN-MME | Comment
4741 Netconf | Required* | PC | PC | Minimum support allowed is Base + Writable Running or Candidate
6241 Netconf | Required* | NC | NC | Obseletes 4741, new features not supported in COM or SGSN-MME
4742 Netconf over SSH | Required* | C | C | 
6242 Netconf over SSH | Required* | NC | NC | Obseletes 4742, new features not supported in COM or SGSN-MME
5539 Netconf over TLS | Allowed | C | NC | 
5277 Notifications | Required | PC | C | COM does not support interleave
5717 Partial Lock | Allowed | NC | NC | Enables fine grained locking
6243 With defaults | Allowed | NC | NC | Unambiguous handling of default attributes
* 4741 or 6241 and 4742 or 6242 are required by EAG

## Slide 33: RFC 4741/6241 Capabilities
Capability | EAG | COM | SGSN-MME | Comment
Base 1.0 (4741) | Required | PC | PC | Session handling, locking, reading, editing
Base 1.1 (6241) |  | NC | NC | 
Writable Running 1.0 | Writable Running or Candidate is required | C | NC | 
Candidate 1.0 |  | NC | C | A “planned area” on the node, PEST study ongoing
Confirmed commit 1.0 | Allowed | NC | NC | 
Confirmed commit 1.1 | Allowed | NC | NC | 
Rollback on error 1.0 | Allowed | C | NC | 
Validate 1.0 | Allowed | NC | C | 
Validate 1.1 | Allowed | NC | NC | 
Start-up 1.0 | Allowed | NC | NC | PEST study ongoing
URL 1.0 | Allowed | NC | NC | 
XPATH 1.0 | Allowed | NC | NC | 

## Slide 34: COM + SGSN-MME Support for Netconf
Support for Netconf is based on RFC 4741
  This is superceded by RFC 6241 which has some small enhancements
Support for Netconf over SSH is based on RFC 4742
  This is superceded by RFC 6242 which has some small enhancements
Support for Netconf Notifications is based on RFC 5277
Support for Netconf over TLS (COM only) is based on RFC 5539
COM + SGSN-MME also provide some proprietary extensions / capabilities to support MO actions, ECIM as data layer …

## Slide 35: Capability exchange + data models
COM supports the <hello> message method for advertising its capabilities
  In theory this should include the MIMs supported by an ME
  This is achieved instead by retrieving the instances of the SysM Schema MOC which indicate per MIM fragment
    The fragment name + version
    The ECIM reference model it is derived from (if applicable)
    A means to access the mp.dtd based XML MIM file
  From OSS-RC perspective we like this approach
    The set of Schema MO’s is used to determine the fragments supported by a given ME (this is not hard-coded at design time)
    This is a key enabler for treated-as support
    It is also an enabler for model driven CM

## Slide 36: Transaction Handling
In COM releases up to 3.3
  A Netconf session is equivalent to a transaction
  Update ME configuration via 1 or more <edit-config> operations
  Close the session via <close-session> operation
  Unless all configuration changes succeed all changes are deleted (due to rollback-on-error capability)
  This violates RFC 4741 where a single <edit-config> operation is a single transaction + closing the session is not needed
In COM 4.0 RFC compliant transaction handling is introduced (more on next slide)
In SGSN-MME an <edit-config> operation is a transaction but only towards the candidate configuration datastore

## Slide 37: Transaction Handling
In COM 4.0 there are 2 Netconf ports per transport protocol
  SSH ports 830 + 1 other port (for use by Ericsson OSS)
  TLS ports 6513 + 1 other port (for use by 3PP OSS)
On ports 830 + 6513 the meaning of the base 1.0 capability is the COM 3.3 level of support for base 1.0
  Additional support is indicated by the ebase capability
  If OSS + COM both support ebase 1.0 (or later) then each <edit-config> is handled as a separate transaction
  If OSS or COM does not support ebase 1.0 (or later) then the old transaction handling behaviour is supported
On the second SSH or TLS ports the meaning of the base 1.0 capability is the RFC 4741 definition of base 1.0 (almost)

## Slide 38: COM support for Netconf
3.1
  Netconf over TLS
  SPI for middleware to report notifications
3.3
  Netconf extensions (not relevant)
4.0 (TCU 14B, Pico RBS 14B)
  Transaction handling
  Improved filter support in <get>, <get-config> + <create-subscription> operations
  Improved error handling for unsupported operations <lock>, <unlock>, <copy-config>, <delete-config>

## Slide 39: SGSN-MME support for Netconf
Has supported Netconf with proprietary data model / data representation for several releases
Support for ECIM introduced in 13B
  ECIM Top, SysM + Application data models only
Support for Netconf notifications in 14A
Other ECIM support
  SwIM in 14A
  SwM in 14B
  PMEventM, PM, BrM … in the roadmap

## Slide 40
Background to Netconf
Overview of Netconf
Netconf Standards
Data Classification and Data Stores
Notifications
COM / SGSN-MME support for Netconf
Further Information

## Slide 41: Further information
Netconf standards: search by RFC number or keyword
COM Netconf IWD: calstore CPI library
  Select CBA Common Components and RDA -> COM -> COM x86_64 -> <COM release> -> <latest shipment>
  Select Interface + then COM Netconf Interface Base document
CBA roadmap (refer to COM section)
SGSN-MME Netconf IWD: 4/155 19-CXC 132 0854
  (Check which version is relevant for which node release)